## Slide 1: Component Based Invisible Computing
IEEE Real-Time Embedded System Workshop
London, December 3, 2001
Johannes Helander <jvh@microsoft.com>
  Microsoft Research
Alessandro Forin, MSR
Paul Pham, MIT
Jagadeeswaran Rajendiran, Duke

## Slide 2: Invisible Computing
Everyday Devices
  Chip makes them better.
  Basic autonomous operation.
  Added value from services.
  Often battery operated.
Device centered, user controlled.
Devices communicate. combination > Σ parts
Small Component Based RTOS.
Standard protocols, Tuned.
Also decomposed PC, smart I/O cards.

## Slide 3: The Operating System (MMLite)
Component Based
  Objects everywhere.
  COM interfaces.
  Unified namespace.
  Same interfaces implemented by many components.
  Multiple implementations of any component.
Specialized to task.
  Pay as you go.
  Late binding and mutation.
  Adaptive to changing requirements.
Real-time scheduling with feedback.
XML based configuration and communication.
Runs on several hardware platforms.

## Slide 4: Communication
RF, TCP/IP, SOAP. Standard protocols. Tuned.
Embedded SOAP prototype:
  COM-Lite automation. XML description.
  Can also deal with messages directly.
  SAX parser. Push model. Process while receiving.
  Code size OK (~16KB parser, tokenizer, marshaller).
  Interoperates with Win2K SOAP Toolkit.
Text parsing takes CPU.
Verbose. Compress?
Drop unnecessary protocol layers.

## Slide 5: Status
Source will be available soon (beta now).
ARM (several versions), i386, H8, MIPS, TriMedia, Map1000, 68k. MMU optional.
Several development boards. Smart I/O cards.
Develop code on simulator under Windows
  Source level debugging of all system features except true RT under Visual Studio. Full speed emulation.
  Cycle-accurate simulators for ARM and TriMedia.
  Use whatever tools available for device → native debuggers often weak.
Sizes e.g. 10KB, 20KB on ARM; 26KB, 160KB on x86. Depends on configuration.
Power e.g. 40mW on 5x7 cm 2.8V ARM board with LCD when playing a simple game (snake).