## Slide 1: Component Based Invisible Computing
12 December 2001, ETH, Zürich
Johannes Helander <jvh@microsoft.com>
  Microsoft Research

## Slide 2: Invisible Computing
Everyday Devices
  Chip makes them better.
  Basic autonomous operation.
  Added value from services.
  Often battery operated.
Device centered, user controlled.
Devices communicate. combination > Σ parts
Small Component Based RTOS.
Standard protocols, Tuned.
Also decomposed PC, smart I/O cards.

## Slide 3: The Operating System (MMLite)
Component Based
  Objects everywhere.
  COM interfaces.
  Unified namespace.
  Same interfaces implemented by many components.
  Multiple implementations of any component.
Specialized to task.
  Pay as you go.
  Late binding and mutation.
  Adaptive to changing requirements.
Real-time scheduling with feedback.
XML based configuration and communication.
Runs on several hardware platforms.

## Slide 4
Object Model
COM
Reference counting
  Simple and non-intrusive
  Has limitations
IUnknown: Base interface
  QueryInterface
  AddRef
  Release
Mutation

## Slide 5
Programming Model
main() returns object, often constructor
Demand-loading namespace
Namespace caches or unloads
Reference count controls lifetime

## Slide 6
Example
VMemAlloc() {
pNS = CurrentNameSpace();
pUnk =pNS->Bind(“VMM”);
pVM = pUnk->QueryInterface(IID_IVmSpace);
pHeap = CreateHeap(pVM);
pHeap->Allocate();
}
IUnknown main() {
pUnk = new();
return pUnk;
}

## Slide 7
MMLite OS == Object System
Full system view (no “kernel”)
Firewalls only when needed
Location transparency
Most everything can be dynamically loaded, unloaded, replaced and/or re-defined
  Loadable virtual memory
  Loadable IPC
  Loadable network
  Loadable drivers

## Slide 8
Mutation in drivers
On PCs: use the BIOS first, load real driver later
Floppy, IDE, SCSI, … anything the PROMs do
Cannot do this with autoconfig

## Slide 9
COM overhead
Overhead acceptable on TriMedia
~~No overhead on x86
Cache eliminates memory fetch

## Slide 10: Communication
RF, TCP/IP, SOAP. Standard protocols. Tuned.
Embedded SOAP prototype:
  COM-Lite automation. XML description.
  Can also deal with messages directly.
  SAX parser. Push model. Process while receiving.
  Code size OK (~16KB parser, tokenizer, marshaller).
  Interoperates with Win2K SOAP Toolkit.
Text parsing takes CPU.
Verbose. Compress?
Drop unnecessary protocol layers.

## Slide 11
Demo1: Smart TAG Scenario
Tag sends token to reader.
Token received. Ask database for matching person data.
Database service sends back identity.
Reader takes personalized action.
Tag knows it was recognized.
SOAP messaging.
Invisible kit [aka MMLite] on Tag, Reader.
Windows 2000 w/ SOAP Toolkit on DB.

## Slide 12
Smart TAG scenario

## Slide 13
MSR Prototype Hardware
The proto hardware has an Atmel AT91FR4081 ARM based microcontroller.
Low power (2.8V, 40 mW).
Runs off 128KB on-chip RAM.
Accelerometer & RF radio (12 kb/s) on second board (5V, 150 mW).
Voltages don’t match. The trend is toward lower voltages.

## Slide 14
Demo4: Remote snake games

## Slide 15: Status
Source will be available soon (beta now).
ARM (several versions), i386, H8, MIPS, TriMedia, Map1000, 68k. MMU optional.
Several development boards. Smart I/O cards.
Develop code on simulator under Windows
  Source level debugging of all system features except true RT under Visual Studio. Full speed emulation.
  Cycle-accurate simulators for ARM and TriMedia.
  Use whatever tools available for device → native debuggers often weak.
Sizes e.g. 10KB, 20KB on ARM; 26KB, 160KB on x86. Depends on configuration.
Power e.g. 40mW on 5x7 cm 2.8V ARM board with LCD when playing a simple game (snake).

## Slide 16
Sizes
Heap (x86 bytes) 2635
PE Loader 4661
Library 3799
Machdep 2086
Timer 1205
ICU 1005
RT-Scheduler 1228
Thread 426
Synchro 1090
Network 84832
VMem 17712
Doom 285696
“Watch”
  minimal
  10 KB on x86
“Cell phone”
  most OS features
  26 KB on x86
  20 KB on arm