## Slide 1: Web Services for Invisible Computing
High volume requires low COGs.
Areas previously unavailable to .NET and GXA
Silicon – street claim: Large footprint and inefficient computing makes GXA unsuitable for embedded use and specialized solutions are required.
False: Web services can be highly efficient while interop and extensibility make the business case.
Proof: By construction. The implementation is efficient, runs on cheap microcontrollers with low footprint.
Energy – street claim: Parsing XML takes lots of CPU and every cycle is x nanojoules.
False: There is no need to transmit ASCII strings as long as the compression is isomorphic to textual XML.
Proof: Prototype pre-tokenized format (multiple versions available) avoids unnecessary conversions. Non-lossy representation is not too difficult.
Be smart about turning off radio when not needed
Bandwidth – street claim: SOAP is bloated and wastes bandwidth.
False: The data can be compressed and delta-encoded while still preserving the virtues.
Proof: Prototype template-based compressor provides encoding isomorphic to textual XML.
Drop unnecessary protocol layers such as HTTP.
Work in progress
Integrate compressed XML with implementation
Finalize solutions in key distribution, mobility, discovery
Challenges: Silicon, energy, bandwidth
Invisible Computing
Computers that are not visible. No install or setup.
Enhance Everyday Devices
  Not primarily a computer. The computer just makes it better.
  Mechanical devices plus networked microcontrollers
  Basic autonomous operation
  Added value from services
  Often battery operated
Device-centered, user controlled
Devices communicate: combination > Σ parts
Small Component Based RTOS
Standard protocols – tuned
Sample Application Areas:
  Home appliances, security, lighting • Family Information Manager
  Wearable Computers • Medical electronics devices
  Sensor networks • Robotics, Industrial Control, Elevators
  Audio Net • Wireless communication gadgets
  Toys • Disaggregated PC, smart I/O cards
System Architecture
The web services and applications are supported by a small RTOS
Combines the good of general-purpose and special-purpose systems
  General purpose in the abstract. Code and interface reuse.
  Special in the concrete. Only take what you need.
Component Based
  Objects everywhere
  COM interfaces
  Unified namespace
  Same interfaces implemented by many components
  Multiple implementations of any component
Specialized to task
  Pay as you go
  Late binding and mutation
  Adaptive to changing requirements
Real-time scheduling with application feedback
XML based configuration and communication
Targeted to microcontrollers
Runs on several hardware platforms
  ARM (many), i386, H8, MIPS, TriMedia, Map1000, 68k, eCOG1
  MMU optional
  Numerous development boards. Prototype gadgets. Smart I/O cards
ROM sizes e.g. 10KB, 20KB on ARM; 26KB, 160KB on x86
Depends on configuration
Power e.g. 40mW on 5x7 cm 2.8V ARM board with LCD when playing a simple game (snake)
Interoperates with ASP+ and SOAP Toolkit on Windows XP
  Implements SOAP 1.1, SOAP 1.2, and WS-Messaging
COM-Lite automation driven by XML description
  Reflection & serialization to and from C and C++
  Can also deal with messages directly
SAX parser. Push model. Process while receiving.
  Shares buffers with network stack. Zero copy networking.
Client and server, P2P
Runs over HTTP and/or UDP with encryption (AES)
  WS-Routing – service path description; replaces HTTP session
Complete TCP/IP, HTTP, SOAP, Automation, RTOS (dynamic memory, threads, etc), drivers, application with complex data.
Runs in 32KB of RAM, 200KB of ROM.
Less if not all components required. Footprint depends on needs. TCP/IP is biggest hog.
Secure Web Services for Invisible Computing
Johannes Helander, Alessandro Forin, Invisible Computing Group, MSR
Demo Setup
An Invisible Computing Scenario
Interoperability
Security
Data analysis
Power
  Bandwidth
  Processing
Routing
Security
Real-Time
Non-graphical UI
Zero-configuration
[VCR]