## Slide 1: Embedded XML Web Services
Realizing a Seamless and Interoperable World through Invisible Computing
Johannes Helander
Researcher
Microsoft Research
March 2, 2005

## Slide 2: Research Agenda
Make deeply embedded devices interoperable with all classes of computers
Extend XML Web Services to new areas
Implement prototype software
Provide Microsoft presence into new area
Add value to PC and services such as ASP.NET

## Slide 3: The Goal: Invisible Computing
Make everyday objects better by adding computation and communication
$5 microcontrollers (32-bit single chip computer)
The computers do their job out of sight
Natural user interface – not screen and mouse
Incremental deployment, no setup hassles
Operate autonomously – added value from services
Devices communicate with each other, PCs, Web

## Slide 4: Sample Applications
Home appliances, security, lighting
Sensor networks
Medical electronic devices
Wearable computers
Robotics, industrial control, national infrastructure
Wireless communication gadgets
Audio net
Disaggregated PC, smart I/O cards
Toys

## Slide 5: Outline
Invisible Computing Devices
Why Web Services?
Our approach
  Table driven serialization
  Compressed SOAP
  Trust and secure discovery
  Distributed real-time
  Componentized RTOS
  Real-time C#
Result
Call to action

## Slide 6
<footer>
<date/time>
An Invisible Computing Scenario
Interoperability
Security
Data analysis
Power
  Bandwidth
  Processing
Routing
Security
Real-Time
Non-graphical UI
Zero-configuration
[VCR]
[Pacemaker]
XP Embedded
[Watch]

## Slide 7: What are Web Services?
The general-purpose solution to communication, in XML
XML is more suitable to computer processing than HTML. Common language for representing any data.
Convergence of EDI, RPC, MSMQ, app specific protocols and formats
All about interoperation. Allows partial understanding
Common protocols obviate need for proxies
Builds on critical mass and momentum

## Slide 8: Do they Scale?
XML Web Services conceived to solve e-business interop problem
Implementations geared towards high-end computers
The same interop problem is the crux of ubiquitous computing
Resource constraints:
  Silicon – footprint
  Energy – parsing overhead
  Bandwidth – size of messages
   Efficient implementation and compression

## Slide 9: Specific Needs
Coordinated real-time computing on multiple devices
  Energy aware protocols (turn off receiver)
Efficient Security and Privacy
Simple setup
Performance

## Slide 10: SOAP example
<soap:Envelope xmlns:soap=http://schemas.xmlsoap.org/soap/envelope/>
<soap:Header
soap:encodingStyle=http://schemas.xmlsoap.org/soap/encoding/>
<wsa:To xmlns:wsa=http://schemas.xmlsoap.org/ws/2004/08/addressing>
http://172.31.46.26/COB/calc.cob
</wsa:To>
</soap:Header>
<soap:Body
soap:encodingStyle=http://schemas.xmlsoap.org/soap/encoding/>
<tns:Add xmlns:tns=http://tempuri.org/Calc/message/>
<A>14</A>
<B>28</B>
</tns:Add>
</soap:Body>
</soap:Envelope>
“Add” two numbers
The calculator is a popular interop test

## Slide 11: Outline
Invisible Computing Devices
Why Web Services?
Our approach
  Table driven serialization
  Compressed SOAP
  Trust and secure discovery
  Distributed real-time
  Componentized RTOS
  Real-time C#
Result
Call to action

## Slide 12: Table Driven Serialization
Processes messages automatically according to description
XML metadata description
  Compiled offline into compact description
  Extensible at runtime
Process while receiving
Zero copy networking
  Serializer & parser share buffers with network stack & crypto
COM-Lite automation
  Turns messages into object calls
  Multiple methods in one message
Multiple transports and encodings
  UDP, HTTP, Encryption, Compression

## Slide 13: Compressed SOAP
Goal: Add(A,B) call should be three bytes
  1) Add 2) A 3) B
Must be convertible to XML mechanically
Must be able to represent any XML
Template based compressor
Onus on discovery process
Process compressed data directly
Simple device only implements what it cares for

## Slide 14: A Secure Invisible Home

## Slide 15: Trust and Discovery
Simple SOAP based trust and service discovery for ad hoc networks
Use “Big” Web Services (WSE/Indigo) when infrastructure present
Optimized for cluster of nodes. Base station (PC) deals with global issues
Public Key Cryptography works on small devices (but can be boosted)
  13s RSA decrypt, 0.03s AES on 25MHz Arm7
  FPGA takes times down by factors of 3000 and 10000 (3ms & 2µs)
Strong crypto necessary for marketability
WS-Security is too bulky

## Slide 16: Setting up a Secure Home
Create house authority, e.g. watch
Touch each device once with watch
  Admits device into trust domain
Discovery process finds device with desired function + does key exchange
  House authority can be offline
  RSA + AES
Write hash of house authority’s key on check to establish trust with bank
 Federation of independent trust domains

## Slide 17: Intuitive Setup
Exploit Context Histories
Trust setup touch based
The touching history is data mined to find proximity clusters
The proximity clusters indicate functional relationship
E.g. touch light-switch and light close together
  automatically ties them together

## Slide 18: Outline
Invisible Computing Devices
Why Web Services?
Our approach
  Table driven serialization
  Compressed SOAP
  Trust and secure discovery
  Distributed real-time
  Componentized RTOS
  Real-time C#
Result
Call to action

## Slide 19: Distributed Real-Time
Coordinated activities
Statistical quality control
Planner
Producer
Consumer
Sensor readings
Scheduling
Scheduling
Sampling

## Slide 20: Real Time...continued
Instigator of activity plans and tunes reservations based on feedback samples
Planner pre-declares future activity at each node
Serialize scheduling trees into XML
Worker nodes accept/reject schedules
Coordinated schedules allow shared resource scheduling. Could turn off radio to save energy
Statistical decision making
Quality control sampling
Concept demo shown at booth #320

## Slide 21: Behavior Patterns
<behavior name="SensorDemo">
<action name="DemoInstigator" endpoint="node:instigator/COB/sensormain.cob">
<message destination="SensorProducer/*"/>
</action>
<action name="SensorProducer" endpoint="node:sensor/COB/sensor.cob"/> <repeat count="100" Period="P1.5S"/>
<message destination="SensorConsumer"/>
</action>
<action name="SensorConsumer“
endpoint="node:consumer/COB/sensor.cob"/>
<repeat count="100" period=”P1.5S”/>
</action>
<sampling destination="node:instigator“
interval="20" number="2"/>
</behavior>
Define the actions and resources for a job
Given to planner

## Slide 22: Task: Instance of Pattern
<task name="SensorDemo-123456">
<action name="SensorProducer“
deadline=”2004-12-11T02:51:48.7001508Z”
tolerance=”P0.005S” duration=”P0.02S”>
<trigger maxCount="100“
offset="P1.5S">SensorProducer</trigger>
</action>
<sampling destination=http://10.10.10.10/feedback
interval="20" number="2"/>
</task>
Specific time and place
Sent to worker by planner

## Slide 23: Resource and Time Estimation
Application specifies confidence needed
Higher confidence costs more resources
estimate
= mean + confidence

## Slide 24: Action Plan
Estimate is predicted by statistical model
Tolerance is medium dependent
estimate
= mean + confidence
tolerance
deadline
latest
start
earliest
start

## Slide 25
Measurements are fed into statistical model
Model predicts future needs
Period k
Time t
k·t0
k·t2
k·t1
1
Fixed producer deadline
Producer
Transmission
Consumer
Action Plan

## Slide 26
Period k
Time t
k·t0
k·t2
k·t1
1
Fixed producer deadline
Producer
Transmission
Consumer
Measurements are fed into statistical model
Model predicts future needs
Timing Adjustment

## Slide 27
Period k
Time t
k·t0
k·t2
k·t1
1
Fixed producer deadline
Producer
Transmission
Consumer
Timing Adjustment
Measurements are fed into statistical model
Model predicts future needs

## Slide 28
Period k
Time t
k·t0
k·t2
k·t1
1
Fixed producer deadline
Producer
Transmission
Consumer
Timing Adjustment
Measurements are fed into statistical model
Model predicts future needs

## Slide 29
Period k
Time t
k·t0
k·t2
k·t1
1
Fixed producer deadline
Producer
Transmission
Consumer
Timing Adjustment
Measurements are fed into statistical model
Model predicts future needs

## Slide 30
Period k
Time t
k·t0
k·t2
k·t1
1
Fixed producer deadline
Producer
Transmission
Consumer
Steady state
Timing Adjustment
Measurements are fed into statistical model
Model predicts future needs

## Slide 31
Time t
k·t0
k·t2
k·t1
1
Fixed producer deadline
Time t
k·t0
k·t2
k·t1
1
Fixed consumer deadline
Sensor to recorder
CD player to speaker
Timing Adjustment
Measurements are fed into statistical model
Model predicts future needs

## Slide 32: Outline
Invisible Computing Devices
Why Web Services?
Our approach
  Table driven serialization
  Compressed SOAP
  Trust and secure discovery
  Distributed real-time
  Componentized RTOS
  Real-time C#
Result
Call to action

## Slide 33: Componentized RTOS
Support for web services on a chip
General purpose in the abstract. Code and interface reuse
Special in the concrete. Only take what you need.
Component-based: objects everywhere
Real-time scheduling with application feedback
XML-based configuration and communication
Hardware platforms
  ARM (many), PPC, i386, MIPS, TriMedia, Map1000, H8, eCOG1
  Numerous development boards, prototype gadgets, smart I/O cards
  “Perfect research platform” elusive

## Slide 34: Real-Time C#
CLR desirable option for embedded systems
Great for extensions, games, apps
Not practical as the exclusive solution in embedded systems
Our real-time scheduling extensions
Prototype C# API implemented
Work-item Scheduler allows mixing native and managed threads
Interpreter execution stacks are multiplexed
No ROM size penalty

## Slide 35: Outline
Invisible Computing Devices
Why Web Services?
Our approach
  Table driven serialization
  Compressed SOAP
  Trust and secure discovery
  Distributed real-time
  Componentized RTOS
  Real-time C#
Result
Call to action

## Slide 36: Microsoft Invisible Computing
A software platform for low cost embedded systems that communicate with each other and with big computers
Research prototype
Has actively been used by academia
Community source license
Complete TCP/IP, HTTP, SOAP, compressed SOAP, real-time SOAP, automation, discovery, trust & security, RTOS (dynamic memory, threads, drivers, etc.), application.
 Runs in computer with 32KB of RAM, 256KB of ROM.
Fewer components  smaller footprint. TCP/IP is biggest hog. Crypto not optimized for size.

## Slide 37: Call to Action
Visit booth #320
Download software from: http://research.microsoft.com/invisible
Use it in products and research
Make your product interoperate with low-cost devices
Talk to jvh