## Slide 1: Microsoft Invisible Computing
Standard protocols – tuned
Embedded SOAP prototype:
  COM-Lite automation driven by XML description
  Can also deal with messages directly
  SAX parser. Push model. Process while receiving
  Code size OK (45KB XML parser, generator; SOAP serializer, deserializer;
    AES, UDP connector)
  Interoperates with WinXP SOAP Toolkit 3.0
  Implements SOAP 1.1 and SOAP 1.2
  Client and server, P2P
Runs over HTTP and UDP with encryption (AES)
WS-Routing – service path description; replaces HTTP session
Text parsing consumes CPU and power
Verbose. Compress?
Drop unnecessary protocol layers
SOAP example
Send calculator add request from PC through HTTP to NTU simulator and ask it to forward to EB63 board using encrypted UDP.
<SOAP-ENV:Envelope xmlns:SOAP-ENV="http://schemas.xmlsoap.org/soap/envelope/">
<SOAP-ENV:Header SOAP-ENV:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">
<m:Path xmlns:m="http://schemas.xmlsoap.org/ws/2002/05/routing">
<m:Action>http://tempuri.org/Calc/action/Calc.</m:Action>
<m:Fwd>
<m:Via>http://172.31.46.26/SOAP/</m:Via>
<m:Via>x-udp-aes-soap://172.31.41.244/SSOAP/COB/calc.cob</m:Via>
</m:Fwd>
<m:Rev><m:Via Vid="1"/></m:Rev>
</m:Path>
</SOAP-ENV:Header>
<SOAP-ENV:Body SOAP-ENV:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">
<m:Add xmlns:m="http://tempuri.org/Calc/message/">
<A>14</A>
<B>28</B>
</m:Add>
</SOAP-ENV:Body>
</SOAP-ENV:Envelope>
Invisible Computing
Everyday Devices
  Chip makes them better
  Basic autonomous operation
  Added value from services
  Often battery operated
Device-centered, user controlled
Devices communicate. combination > Σ parts
Small Component Based RTOS
Standard protocols
Sample Application Areas:
  Wearable Computers • Medical electronics devices
  Sensor networks • Industrial Control
  Elevators • Home appliances, security, lighting
  Robotics • Wireless communication gadgets
  Toys • Decomposed PC, smart I/O cards
Operating System Architecture
Component Based
  Objects everywhere
  COM interfaces
  Unified namespace
  Same interfaces implemented by many components
  Multiple implementations of any component
Specialized to task
  Pay as you go
  Late binding and mutation
  Adaptive to changing requirements
Real-time scheduling with application feedback
XML based configuration and communication
Runs on several hardware platforms
Microsoft Research
WS-Routing provides service level routing of SOAP messages
  One-way
  RPC
  P2P
  Asymmetric messaging
  Schema converter (inter-version service)
  Protocol converter
Provides header for object URL, continuation passing
WS-Routing examples
Status
Source will be available soon (beta now)
ARM (several versions), i386, H8, MIPS, TriMedia, Map1000, 68k. MMU optional
Several development boards. Smart I/O cards
Develop code on simulator under Windows
  Source level debugging of all system features except true Real-Time
  under Visual Studio. Supports full speed emulation
  Cycle-accurate simulators for ARM and TriMedia
  Use whatever tools available for device → native debuggers often weak
Sizes e.g. 10KB, 20KB on ARM; 26KB, 160KB on x86 Depends on configuration
Web services run on eb63 board (low-end ARM, 256KB RAM)
Power e.g. 40mW on 5x7 cm 2.8V ARM board with LCD
when playing a simple game (snake)
Secure Web Services for Invisible Computing
Alessandro Forin, Johannes Helander, Amit Vyas, Yong Xiong
An Invisible Computing Scenario
Interoperability
Security
Data analysis
Power
  Bandwidth
  Processing
Routing
Security
Real-Time
Non-graphical UI
Zero-configuration
Demo Setup